## Slide 1
26-2 Special Topics in Naval Architecture · Team 5
AIS Track-based Traffic Analysis of a Port Approach Channel
& selection of monitoring priority zones — Norfolk / Hampton Roads, USA
1st Proposal
고영조 · 김희선 · 백지원 · 조민제
Priority Zone Monitor
2024
Grid size
500 m
Vessel groups
Cargo · Tanker
Candidate rule
Top 10% unique MMSI
Notes: Title. Team 5 first proposal: AIS track-based traffic analysis of the Norfolk / Hampton Roads port approach and selection of monitoring priority zones. Members: Ko Youngjo, Kim Heeseon, Baek Jiwon, Cho Minje.

## Slide 2: Meet the team
02 — TEAM
고
고영조
[Major / lab]
[Research interest]
Role · TBD
김
김희선
[Major / lab]
[Research interest]
Role · TBD
백지원
Ph.D. Candidate
Scheduling · MARL
Role · TBD
조
조민제
[Major / lab]
[Research interest]
Role · TBD
Notes: Team introduction. Fill in each member's background and research interest; roles will be finalized after the initial data check.

## Slide 3: Why port approach channels?
03 — PROBLEM OVERVIEW
Traffic converges at a chokepoint
Cargo ships, tankers, tugs and naval vessels all squeeze into the same approach lanes.
Monitoring resources are limited
Patrol and VTS attention must go where — and when — traffic actually concentrates.
AIS makes it measurable
A full year of open AIS tracks gives MMSI, time and vessel group for every track.
RESEARCH QUESTIONS
RQ1
Where do observed vessels concentrate around the approach channel?
RQ2
How much do cargo and tanker routes overlap — and how does it shift by month?
RQ3
Do the priority zones hold when grid size and selection cut-off change?
Notes: Why this problem: approach channels are chokepoints shared by many vessel types; monitoring resources are limited, so we need evidence on where and when traffic concentrates; NOAA AIS Vessel Tracks 2024 makes this quantitative. Three research questions guide the work.

## Slide 4: Four steps to priority zones
04 — WORK PLAN
01
Data build & preprocessing
Clip to study area
Check missing records
Reproject to UTM
→ Clean dataset
Owner · TBD
02
Traffic characterization
Routes by group
Monthly unique ships
Tracks vs. MMSI
→ Route maps · stats
Owner · TBD
03
Priority zone selection
500 m grid count
Top 10% = candidates
Cargo–tanker overlap
→ Priority map + table
Owner · TBD
04
Robustness check
Grid 250 m – 1 km
Cut-off 10% vs. 20%
Overlap area & shift
→ Stable vs. fragile zones
Owner · TBD
Notes: Plan: (1) data build and preprocessing, (2) traffic characterization, (3) monitoring priority zone selection, (4) robustness check. Each step has an owner slot — role assignment to be finalized.

## Slide 5: What is in the AIS track dataset
05 — AIS DATA OVERVIEW
GeoPackage
file format
SQLite container (.gpkg)
1 layer
feature layer
AISVesselTracks2024
11 fields
per row
10 attributes + Shape
EPSG:4269
coordinates
NAD83 lon / lat
VesselGroup — broad source category
Cargo
Tanker
Fishing
Passenger
…
Dark = in scope for this study
HOW ROWS ARE FORMED
1 row = 1 track interval. One vessel (MMSI) appears in many rows.
MMSI 563156300
row 1
row 2
row 3
row 4
gap
Illustrative timeline
Raw AIS sampled to 1 min
→ new track when gap > 30 min or > 1 NM
→ built per month and per ocean basin
Notes: AIS Vessel Tracks 2024 is a GeoPackage — a SQLite database holding features, attributes, CRS metadata and spatial indexes. Its single feature layer, AISVesselTracks2024, has 11 fields: 10 attributes plus the Shape geometry, in EPSG:4269 (NAD83 lon/lat). Each row is a track for one time interval, so one vessel (MMSI) appears in many rows: raw AIS is sampled to one minute and a new track starts after a 30-minute or 1-nautical-mile gap. VesselGroup gives a broad category; we keep Cargo and Tanker.

## Slide 6: Inside the GeoPackage file
05 — AIS DATA OVERVIEW
AISVesselTracks2024.gpkg SQLite container
Spatial index
rtree_AISVesselTracks2024_Shape
Bounding box of every track → fast candidate lookup
Feature layer
AISVesselTracks2024
10 attributes + Shape (MULTILINESTRING) per row
Metadata tables
gpkg_contents · gpkg_spatial_ref_sys
Layer description and CRS: EPSG:4269
1
BBox lookup
RTree returns candidate tracks
2
Exact intersect
Drop bbox-only false positives
3
Cargo & Tanker
Filter on VesselGroup
4
pandas chunks
Read 100k rows at a time
5
CSV + Shape_WKT
Binary geometry → WKT text
Blue dashed arrows: which part of the file each step relies on
Notes: The downloaded archive holds one GeoPackage, a SQLite container with three parts: the feature layer AISVesselTracks2024 (attributes plus MULTILINESTRING Shape geometry), GeoPackage metadata tables (layer and CRS, EPSG:4269), and an RTree spatial index on Shape. Our extract uses the RTree for a fast bounding-box candidate lookup, then an exact geometry intersection to remove false positives, filters Cargo and Tanker on VesselGroup, reads the result in pandas chunks, and writes a CSV where the binary Shape is converted to WKT text in Shape_WKT. The CRS label is carried in a Geometry_CRS column because CSV does not keep CRS metadata.

## Slide 7: Structure of raw data — one row, one line
05 — AIS DATA OVERVIEW
Field | Type | Meaning | Use
Shape | MultiLineString | Track line (can have several parts) | CORE
MMSI | Medium int | Vessel ID — recurs across rows | CORE
TrackStartTime | Date/time | Start of track interval | CORE
TrackEndTime | Date/time | End of track interval | CORE
VesselGroup | Text (25) | Broad category: Cargo, Tanker … | CORE
VesselType | Medium int | Type code (needs codebook) | SUPPORT
Length · Width · Draft | Double | Vessel dimensions as reported | SUPPORT
DurationMinutes | Medium int | Track duration in minutes | SUPPORT
OBJECTID | Integer | Row ID, used by spatial index | DROP
11 fields in total (Length, Width, Draft shown in one row)
OBJECTID 50958 · MMSI 563156300 · Cargo
2024-01-01 00:02 → 01-06 19:59 UTC
Notes: Each row carries one vessel track for a time interval. Shape holds the whole line; MMSI identifies the vessel and repeats across rows; start/end time bound the interval; VesselGroup gives the broad category. VesselType is only a numeric code and needs a codebook before we interpret it. OBJECTID is a row identifier used by the spatial index. The map shows one real row from our first-pass extract: OBJECTID 50958, MMSI 563156300, a Cargo track from 1 to 6 January 2024. Reference points are approximate and there is no coastline layer; the line was redrawn from the extract plot.

## Slide 8: First-pass extract — Hampton Roads
05 — AIS DATA OVERVIEW
10,943
track rows
Cargo + Tanker, 2024
CSV ≈ 373 MB
Cargo 94.2%
Tanker 5.8% of rows
CARGO
1,865 vessels (MMSI)
10,311 rows · ≈5.5 rows / vessel
TANKER
138 vessels (MMSI)
632 rows · ≈4.6 rows / vessel
Filter
lon −77.0 → −75.5, lat 36.3 → 37.5 (EPSG:4269)
Rule
Keep tracks that intersect — whole line kept, not clipped
CSV adds
Shape_WKT · Geometry_CRS · Subset_BBox
Temporary broad rectangle — not the final study boundary
Notes: First-pass extract: we kept every Cargo or Tanker track whose geometry intersects a broad rectangle from longitude −77.0 to −75.5 and latitude 36.3 to 37.5. That gives 10,943 rows: 10,311 Cargo rows from 1,865 distinct vessels and 632 Tanker rows from 138 vessels — about five rows per vessel, which is why we count unique MMSI separately from tracks. The CSV is about 373 MB and adds Shape_WKT, Geometry_CRS and Subset_BBox. The rectangle is temporary, not the final study boundary, and tracks crossing its edge are kept whole.

## Slide 9: From national tracks to a regional dataset
06 — DATA PREPROCESSING
DATA SCOPE
Source
NOAA MarineCadastre AIS Vessel Tracks 2024 [1]
Period
Jan – Dec 2024
Area
Now: broad rectangle → next: NOAA ENC-based approach boundary [3]
Vessels
Cargo & Tanker — source label is “Cargo”, not Bulk_Carrier
Data
Raw .gpkg kept unchanged; CSV is a re-creatable interim file
1. Spatial-index extract
RTree + exact intersection on the rectangle
DONE
2. Filter vessel groups
Cargo & Tanker → 10,943 rows
DONE
3. Confirm study boundary
ENC-based approach area, then rerun the filter
NEXT
4. Resolve vessel-type scope
VesselType codebook; all Cargo or a sub-type?
NEXT
5. Clip or keep whole + QC
Per analysis; missing MMSI / time, invalid paths
NEXT
6. Reproject & build dataset
EPSG:4269 → UTM 18N; GeoPandas → GeoParquet
NEXT
[1] NOAA OCM, AIS Vessel Tracks 2024 [3] NOAA OCS, Electronic Navigational Charts
Notes: Main data: NOAA MarineCadastre AIS Vessel Tracks 2024, Jan–Dec 2024. Done so far: spatial-index extract on a broad rectangle and the Cargo/Tanker filter, giving 10,943 rows. Next: confirm the study boundary from NOAA ENCs and rerun the filter; decide whether we target all Cargo or a narrower type, using a VesselType codebook (the source says Cargo, not Bulk_Carrier); decide per analysis whether tracks are clipped or kept whole, and run quality checks; then reproject to UTM 18N and build the Python dataset. The raw GeoPackage stays unchanged and the CSV can be regenerated from the documented filter.

## Slide 10
07 — EXPECTED OUTCOMES
What the priority-zone map enables
DELIVERABLES
✓ Route maps by vessel group
✓ Monthly traffic statistics
✓ Priority zone map & table
✓ Robustness report across criteria
Efficient maritime patrol
Allocate patrol and VTS attention to zones that persist across months and criteria.
Spot ghost / illicit vessels
Use the normal-traffic baseline to flag tracks that vanish or stray in busy zones.
Early collision-risk alerts
Zones where cargo and tanker lanes overlap become candidates for warnings.
Channel maintenance
Prioritize inspection, dredging and aids-to-navigation upkeep on busy lanes.
Scope note: priority zones are observation candidates from historical traffic — not collision probabilities or real-time decisions. Track counts ≠ port calls.
Notes: Expected insights: efficient maritime patrol, detection of ghost / illicit vessels, early warning for collision-risk zones, and maintenance prioritization for heavily used lanes. Limitation: AIS tracks can be split by reception gaps, so track counts are not port calls; spatial overlap of paths does not mean simultaneous encounters. The priority zones are observation candidates, not collision probabilities.